## Slide 1
AKVORADO · FLOW COLLECTION LAB
Akvorado Lab.
Deploying a flow collection stack with Docker — for the network engineers who'll actually run it.
Don Jolley · ZANOG
workshop · 60 min · hands-on

## Slide 2
akvorado lab
01 · intro
BY THE END OF THIS SESSION
A working flow stack — and the intuition to keep it running.
01
A fully operational Akvorado stack running in Docker on your lab VM.
02
At least one network device exporting flows into your collector.
03
Verified traffic visibility in the Akvorado web interface.
04
A clear mental model of NetFlow, sFlow, and sample rate trade-offs.
akvorado-lab · don jolley
slide 02

## Slide 3
akvorado lab
01 · intro
AGENDA
Eight sections, one running stack.
§ 01
Flow fundamentals — what NetFlow and sFlow actually do
§ 02
Sample rate math — sizing the router, collector, and disk
§ 03
Stand up the Docker stack on a fresh VM
§ 04
Configure MikroTik, Arista, Juniper, Cisco
§ 05
Verify flows are actually arriving
§ 06
Troubleshoot when they aren't
§ 07
Production hardening — TLS and basic auth
§ 08
Tear it all down cleanly
akvorado-lab · don jolley
slide 03

## Slide 4
§ 01
Flow fundamentals
Before any config — what your router actually sends, and why it sends it that way.

## Slide 5
§ 01 fundamentals
flow basics
FLOW · NOUN
A summary of traffic between two endpoints.
Your router watches packets pass through an interface, groups them by 5-tuple, and periodically exports a summary record. The collector never sees the packets themselves — only the summaries.
FULL PACKET CAPTURE
Every byte, every packet, every header.
Storage cost: catastrophic.
FLOW RECORDS
Per-conversation summaries, exported on a timer.
Storage cost: tractable.
akvorado-lab · don jolley
slide 05

## Slide 6
§ 01 fundamentals
record fields
ONE RECORD · MANY FIELDS
Anatomy of a flow record.
FIELD
EXAMPLE
Source IP
192.168.1.10
Destination IP
8.8.8.8
Protocol
TCP
Source port
54321
Destination port
443
Bytes transferred
142,400
Packets
98
Interface (in/out)
ether1
Timestamp
2024-03-15 10:23:01
akvorado-lab · don jolley
slide 06

## Slide 7
§ 01 fundamentals
netflow
NETFLOW
A family, not a single protocol.
Cisco invented it; everyone else implemented variants. Three versions you'll encounter in the wild.
VERSION
WHAT IT IS
v5
Oldest. Fixed record format. IPv4 only. Still widely supported.
v9
Template-based. Supports IPv6, MPLS, BGP fields. Flexible — and what we'll use today.
IPFIX
"NetFlow v10" — the IETF standard. Most extensible.
MikroTik's Traffic Flow feature speaks v5 and v9. We're picking v9.
akvorado-lab · don jolley
slide 07

## Slide 8
§ 01 fundamentals
export mechanics
NETFLOW EXPORT
Cache, expire, ship.
01
Router sees a new flow on a monitored interface.
02
It tracks the flow in a local cache.
03
When the flow ends (TCP FIN/RST) or a timer fires, the record is exported to the collector.
04
Records are sent over UDP. If a packet is dropped, the record is lost.
TWO TIMERS TO KNOW
ACTIVE TIMEOUT
Forces an export for long-lived flows that haven't ended yet — typically every 60 s.
INACTIVE TIMEOUT
Exports a record once a flow has gone idle — typically 15 s.
akvorado-lab · don jolley
slide 08

## Slide 9
§ 01 fundamentals
sflow
SFLOW · SAMPLED FLOW
sFlow samples; NetFlow tracks.
Rather than maintaining a flow cache, sFlow takes statistical packet samples directly from the hardware forwarding plane.
01
The switch samples 1 in every N packets — e.g. 1 in 1024.
02
Each sampled packet is encapsulated with interface counters and sent as a UDP datagram.
03
The collector extrapolates total traffic from the samples.
WHY IT SCALES
Sampling happens in the ASIC, not the CPU. The control plane only sees the datagrams it has to export — never every packet that ever crossed an interface.
This is why sFlow can ride 100 G interfaces without breaking a sweat.
akvorado-lab · don jolley
slide 09

## Slide 10
§ 01 fundamentals
compare
SIDE BY SIDE
NetFlow vs sFlow.
NETFLOW / IPFIX
SFLOW
Method
Flow cache tracking
Packet sampling
Accuracy
Exact for tracked flows
Statistical
Hardware need
Flow cache in software / ASIC
Very low — ASIC handles it
High-speed fit
Can struggle at high rates
Built for it
Header depth
Flow metadata only
Includes packet header payload
Use both. Akvorado happily ingests them side by side on different ports.
akvorado-lab · don jolley
slide 10

## Slide 11
§ 01 fundamentals
ports
REMEMBER THESE THREE
Default UDP ports.
2055
NETFLOW V5 / V9
Our MikroTik will send here
4739
IPFIX
The IETF standard port
6343
SFLOW
Our Arista will send here
Akvorado's inlet component listens on all three.
akvorado-lab · don jolley
slide 11

## Slide 12
§ 02
Sample rate math.
One number. Three downstream costs. Get the intuition right and you'll never argue about it again.

## Slide 13
§ 02 sample rate
semantics
READ THIS CAREFULLY
What 1:1024 actually means.
The hardware forwards one packet out of every 1024 to the sFlow agent for export.
Selection is random — not every 1024th packet in sequence.
Random selection is what gives the samples statistical validity.
The collector multiplies observed bytes by N to estimate the wire total.
WORKED EXAMPLE
# one sampled packet, 1500 bytes, rate = 1:1024 1500 B × 1024 ≈ 1.5 MB # that single sample represents # ~1.5 MB of wire traffic.
akvorado-lab · don jolley
slide 13

## Slide 14
§ 02 sample rate
cost · switch
WHERE DOES THE WORK HAPPEN?
Sampling is free. Exporting isn't.
The ASIC does the sampling — that's why sFlow scales. But encapsulating and shipping the datagrams still touches the control plane.
datagrams exported per second · 1 Gbps · avg 500 B packet
SAMPLE RATE
PACKETS/SEC
EXPORTED DATAGRAMS/SEC
CONTROL-PLANE LOAD
1:64
~250,000
~3,900
heavy
1:512
~250,000
~490
comfortable
1:1024
~250,000
~245
light
1:4096
~250,000
~61
trivial
Line rate doesn't change — only the export rate does. 1:512 to 1:1024 is a safe starting range on a 1 G interface.
akvorado-lab · don jolley
slide 14

## Slide 15
§ 02 sample rate
cost · collector
AKVORADO + KAFKA
CPU scales with datagrams, not with line rate.
Every datagram gets parsed, enriched (SNMP, GeoIP, AS lookup), and pushed onto Kafka. That work is per-datagram — the underlying 10 G or 100 G is irrelevant.
LOW RATE · 1:64
High datagram rate. High CPU and memory pressure on the collector. More enrichment lookups per second.
HIGH RATE · 1:4096
Low datagram rate. Very low collector load — but coarser visibility. Small flows may be missed entirely.
For a lab with light traffic, 1:256 or 1:512 gives you visible results fast without overwhelming anything.
akvorado-lab · don jolley
slide 15

## Slide 16
§ 02 sample rate
cost · storage
CLICKHOUSE · ROWS PER DAY
Lower sample rate, bigger disk.
Every enriched record from Kafka becomes a row in ClickHouse. Storage is directly proportional to samples received.
# mental model rows_per_day = (avg_pps) × 86,400 ÷ sample_rate
ClickHouse compresses columnar data efficiently — but write amplification at very low N is still real.
Lower N means more rows, more I/O, faster disk growth.
Higher N means coarser data — but a stack you can leave running for months.
akvorado-lab · don jolley
slide 16

## Slide 17
§ 02 sample rate
worked example
DO THE MATH · THE DIFFERENCES ARE HUGE
50,000 pps across all interfaces.
AT 1:1024
50,000 × 86,400 ÷ 1024 ≈ 4.2 M rows/day # 50–150 bytes/row after compression ≈ 200–600 MB/day
Easily manageable. Months of data on a small disk.
AT 1:64
50,000 × 86,400 ÷ 64 ≈ 67.5 M rows/day # same compression assumption ≈ 3–10 GB/day
Same traffic. 16× the storage cost.
akvorado-lab · don jolley
slide 17

## Slide 18
§ 02 sample rate
choosing
MATCH RATE TO INTERFACE
Pick N from your link speed.
SCENARIO
SUGGESTED RATE
RATIONALE
Lab · light traffic
1:256 – 1:512
See data quickly, minimal load
Production · 1 G
1:1024
Balance of visibility and load
Production · 10 G
1:2048 – 1:4096
Prevents collector overload
Production · 100 G
1:8192 – 1:16384
ASIC handles it; keep datagram rate sane
akvorado-lab · don jolley
slide 18

## Slide 19
§ 02 sample rate
heuristic
IF YOU REMEMBER NOTHING ELSE
Aim for the comfort zone.
200–500
SFLOW DATAGRAMS PER SECOND, PER INTERFACE
Work backwards from your expected packet rate to pick N.
N ≈ avg_pps ÷ 300
300 datagrams/sec is right in the middle of comfortable. Anything in the 200–500 band is fine.
akvorado-lab · don jolley
slide 19

## Slide 20
§ 03
Stand up the stack.
From bare Ubuntu VM to running Akvorado console in roughly ten minutes of typing.

## Slide 21
Summary
Update system
Install Docker
Add user to docker group
Mkdir and pull quick start script
Edit Config/outlet.yml file with correct SNMP string
Start stack.
Make sure interfaces on routers match correct description

## Slide 22
§ 03 stand up
topology
OUR LAB
Lab topology.
NETWORK DEVICES
— MikroTik router
— Arista switch
flow export · UDP
──▶
LAB VM
DOCKER COMPOSE STACK
akvorado · inlet
akvorado · console
kafka
clickhouse
Web UI → http://VM-IP:8081
akvorado-lab · don jolley
slide 21

## Slide 23
§ 03 stand up
VM specs
BEFORE YOU START
Give the VM enough room.
RESOURCE
MINIMUM
RECOMMENDED
OS
Ubuntu 22.04 LTS
Ubuntu 24.04 LTS
CPU
2 vCPUs
4 vCPUs
RAM
4 GB
8 GB
Disk
20 GB
40 GB
Network
1 NIC, reachable from devices
Static IP assigned
20 GB is fine for this lab. Don't use it as a production sizing reference — ClickHouse is hungry.
akvorado-lab · don jolley
slide 22
Tested on Ubuntu 26.04

## Slide 24
§ 03 stand up
firewall
UFW OR YOUR FIREWALL OF CHOICE
Three ports inbound.
PORT
PROTO
PURPOSE
2055
UDP
NetFlow v5/v9 — MikroTik
6343
UDP
sFlow — Arista
8081
TCP
Akvorado Web UI
open them with ufw
$ sudo ufw allow 2055/udp $ sudo ufw allow 6343/udp $ sudo ufw allow 8081/tcp $ sudo ufw status
akvorado-lab · don jolley
slide 23

## Slide 25
§ 03 stand up
docker
FROM DOCKER'S OWN REPOSITORY
Install Docker Engine + Compose.
add the docker repo
$ sudo install -m 0755 -d /etc/apt/keyrings # fetch and dearmor the GPG key $ curl -fsSL \
https://download.docker.com/linux/ubuntu/gpg \
| sudo gpg --dearmor \
-o /etc/apt/keyrings/docker.gpg
# register the source list $ echo "deb [...] stable" | \
sudo tee /etc/apt/sources.list.d/docker.list
install and enable
$ sudo apt-get update $ sudo apt-get install -y \
docker-ce docker-ce-cli \
containerd.io \
docker-buildx-plugin \
docker-compose-plugin
$ sudo usermod -aG docker $USER
$ sudo systemctl enable --now docker
Log out and back in for the group change to take effect.
akvorado-lab · don jolley
slide 24

## Slide 26
§ 03 stand up
quickstart
GRAB THE VERSION-MATCHED BUNDLE
Working directory & quickstart bundle.
Akvorado ships a quickstart tarball with each release — a complete, version-matched compose file and example configs. Use it.
$ mkdir ~/akvorado && cd ~/akvorado # download the latest quickstart tarball $ URL=https://github.com/akvorado/akvorado/releases/latest $ curl -sL $URL/download/docker-compose-quickstart.tar.gz \
| tar zxvf -
# see what you got $ ls -lh
If your lab pack ships its own docker-compose.yml with TLS & basic auth pre-applied — copy it over the extracted one.
akvorado-lab · don jolley
slide 25

## Slide 27
§ 03 stand up
services
WHAT THE COMPOSE FILE GIVES YOU
Four services. One stack.
akvorado
The main application — inlet, orchestrator, console.
clickhouse
The columnar database that stores every enriched flow row.
kafka
The message queue between the inlet and ClickHouse. Buffers spikes.
REDIS /
Proxy
Web services.
Open the file before you start anything — cat docker-compose.yml — and identify each service.
akvorado-lab · don jolley
slide 26

## Slide 28
§ 03 stand up
service flow
DATA PATH INSIDE THE STACK
Service flow.
FLOW PACKETS
UDP from your devices
▼
AKVORADO · INLET
parse · enrich · SNMP · GeoIP · AS
▼
KAFKA
durable queue
▼
AKVORADO · ORCHESTRATOR
writes rows
──▶
CLICKHOUSE
columnar store
▼
AKVORADO · CONSOLE
web UI on :8081
akvorado-lab · don jolley
slide 27

## Slide 29
§ 03 stand up
config · snmp
OPTIONAL · HIGHLY RECOMMENDED
Give your interfaces names.
Without SNMP, your flows arrive labelled by ifIndex. With it, you get ether1 and Ethernet1 — readable in the UI.
metadata:
providers:
- type: snmp
credentials:
::/0:
communities:
- public
- private
HEADS UP
The config schema drifts between releases. The example file in the tarball is the authoritative reference for the version you're running.
akvorado-lab · don jolley
slide 29

## Slide 30
§ 03 stand up
iterate fast
DON'T BOUNCE THE WHOLE STACK
Restart only what changed.
Config files are bind-mounted from the host. The container already has the new file — it just needs to re-read it on startup.
config file changed
$ docker compose restart \
akvorado-outlet
$ docker compose restart \
akvorado-inlet
$ docker compose restart \
akvorado-orchestrator
A few seconds. ClickHouse and Kafka stay up.
docker-compose.yml itself changed
# ports, env vars, mounts # need a recreate, not a restart $ docker compose up -d \
--force-recreate \
akvorado-outlet
Restart ≠ recreate. Know the difference.
akvorado-lab · don jolley
slide 30

## Slide 31
§ 03 stand up
launch
THE MOMENT OF TRUTH
Pull, start, verify.
$ cd ~/akvorado $ docker compose up -d # first run will pull images — give it a few minutes $ docker compose ps NAME STATUS akvorado-inlet running akvorado-console healthy clickhouse healthy redpanda running
Open http://<YOUR-VM-IP>:8081 — the UI will be empty until flows arrive.
akvorado-lab · don jolley
slide 31

## Slide 32
§ 04
Send us some flows.
Four vendors, four config dialects. Replace every <AKVORADO-VM-IP> with your VM's address.

## Slide 33
§ 04 devices
mikrotik · netflow
ROUTEROS · /IP TRAFFIC-FLOW
MikroTik — Traffic Flow.
# enable Traffic Flow on all interfaces /ip traffic-flow set enabled= yes interfaces=all \
active-flow-timeout=
1m inactive-flow-timeout=15s # pin the export version /ip traffic-flow version set version= 9 # point it at akvorado /ip traffic-flow target add dst-address= <AKVORADO-VM-IP> port=2055 version=9
Verify with /ip traffic-flow print and /ip traffic-flow target print.
akvorado-lab · don jolley
slide 33

## Slide 34
§ 04 devices
mikrotik · names
A QUIRK WORTH KNOWING
Interface comments become interface names.
MikroTik exports the Comment field — not the identifier (ether1 ). No comment, no readable name in Akvorado.
# set a meaningful comment on every monitored interface /interface set ether1 comment="WAN-Upstream" /interface set ether2 comment="LAN-Core"
Do this before sending flows. Otherwise your dashboards are full of blank labels and indexes.
akvorado-lab · don jolley
slide 34

## Slide 35
§ 04 devices
mikrotik · gotcha
ROUTEROS V7 · THE TRAP
v7 omits the sampling rate field.
RouterOS v7 doesn't include the sampling rate in its v9 export. Akvorado can't scale traffic correctly — flow volumes appear orders of magnitude lower than reality.
tell akvorado what mikrotik forgot · config/outlet.yaml
core :
default-sampling-rate: 1
1 means every packet is tracked — correct for NetFlow. MikroTik records every flow, it just forgets to mention it.
$ docker compose restart akvorado-outlet
akvorado-lab · don jolley
slide 35

## Slide 36
§ 04 devices
arista · sflow
EOS · NATIVE ASIC SAMPLING
Arista — sFlow.
! configure terminal
! 1 in every 1024 packets sflow sample 1024
! interface counter polling, in seconds sflow polling-interval 30
! collector destination sflow destination <AKVORADO-VM-IP> 6343
! turn it on globally sflow run
! enable per-interface (repeat as needed)
interface Ethernet1
sflow enable
akvorado-lab · don jolley
slide 36

## Slide 37
§ 04 devices
arista · full
PRODUCTION-SHAPED EOS CONFIG
Arista — the real-world config.
sflow sample 4096 sflow sample truncate size 200 sflow polling-interval 20 sflow destination {ip_v4_address} 6343 sflow source-interface Loopback0
sflow extension bgp
no sflow extension router
sflow interface disable default
sflow run
interface Eth1/1
sflow enable
sflow egress enable
Verify with show sflow and show sflow interfaces.
akvorado-lab · don jolley
slide 37

## Slide 38
§ 05
Verify.
Three places to look. From the wire to the dashboard.

## Slide 39
§ 05 verify
inlet logs
FIRST PLACE TO CHECK
Watch the inlet logs.
Within 1–2 minutes of configuring a device — depending on its active-flow timeout — you should see records arriving.
$ docker compose logs -f akvorado \
| grep -i
"flow\|inlet\|receive" akvorado-inlet | received 412 netflow records from 10.0.0.1 akvorado-inlet | received 28 sflow samples from 10.0.0.2 akvorado-inlet | snmp: resolved ifIndex 3 → "WAN-Upstream"
akvorado-lab · don jolley
slide 41

## Slide 40
§ 05 verify
wire check
WHEN IN DOUBT, DROP TO THE WIRE
tcpdump on the VM, not in the container.
If the inlet logs are silent, prove flows are even reaching the VM before blaming the stack.
incoming netflow
$ sudo tcpdump -i any \
udp port
2055 -n
incoming sflow
$ sudo tcpdump -i any \
udp port
6343 -n
INTERPRETING RESULTS
Packets here but nothing in Akvorado → problem is inside the container stack. No packets → the device isn't sending, or a firewall is in the way.
akvorado-lab · don jolley
slide 42

## Slide 41
§ 05 verify
web ui
HTTP://<VM-IP>:8081
The UI comes alive.
Within a few minutes of flows arriving, refresh the console and you should see —
01
Source and destination IPs populating the sankey diagram.
02
Traffic volume graphs starting to build.
03
Interface names appearing — if SNMP enrichment is configured.
If you don't see this within five minutes, the next section is for you.
akvorado-lab · don jolley
slide 43

## Slide 42
§ 06
When it goes wrong.
A checklist and a nuclear option.

## Slide 43
§ 06 troubleshoot
checklist
WORK THROUGH IT IN ORDER
Troubleshooting checklist.
CHECK
COMMAND
Are packets reaching the VM?
sudo tcpdump -i any udp port 2055
Is the inlet running?
docker compose ps
Is the config file mounted correctly?
docker compose exec akvorado cat /etc/akvorado/akvorado.yaml
Are there errors in the inlet log?
docker compose logs akvorado
Is ClickHouse accepting writes?
docker compose logs clickhouse
Port conflicts on the host?
sudo ss -ulnp | grep -E "2055|6343|8081"
akvorado-lab · don jolley
slide 45
Check SNMP settings match on the device and in the outlet.yaml file
Check that the router is allowing SNMP polling from the VM
Check that the interface description matches the regex in the outlet.ymal file

## Slide 44
§ 06 troubleshoot
nuclear option
WHEN NOTHING ELSE WORKS
Reset the stack — wipe everything.
$ cd ~/akvorado
$ docker compose down -v
$ docker compose up -d
WARNING
-v
deletes the data volumes. Every flow record you've collected is gone.
Use this when the stack is in an unrecoverable state — not as a first response.
akvorado-lab · don jolley
slide 46

## Slide 45
§ 07
Production hardening.
HTTP on 8081 is fine for a lab. It is not fine on the open internet. Let's Encrypt + basic auth, via Traefik.

## Slide 46
§ 07 harden
diff
FOUR AREAS TO TOUCH
What changes for production.
AREA
DEFAULT
SECURED
Traefik entrypoints
HTTP :8081 only
:80 redirect · :443 HTTPS · :8080 private
TLS
None
Let's Encrypt · ACME HTTP challenge
Authentication
None
bcrypt basic auth on websecure
Console router
HTTP only
HTTPS, cert resolver, domain
Volumes
No cert storage
akvorado-letsencrypt
All changes live inside docker-compose.yml. The Akvorado containers themselves don't change.
akvorado-lab · don jolley
slide 48

## Slide 47
§ 07 harden
prereqs
NON-NEGOTIABLE
Three things must be true.
01
A public DNS A record points to your VM — e.g. flows.example.com → 1.2.3.4.
02
Ports 80 and 443 are open on the VM's firewall.
03
Let's Encrypt can reach the VM over HTTP — so a private/internal IP won't work.
RATE LIMITS
Let's Encrypt allows 5 certs per domain per week on production. Test against the staging endpoint first — set
ACME_CASERVER
to the staging URL until your config is right.
akvorado-lab · don jolley
slide 49

## Slide 48
§ 07 harden
auth · bcrypt
BASIC AUTH · STORED AS BCRYPT
Generate the password hash.
$ sudo apt-get install -y apache2-utils # -n: write to stdout · -b: password on cli · -B: bcrypt $ htpasswd -nbB flows yourpassword flows:$2y$05$LbR0WmEdIsh0Z8Mv2o2p1uGLN3ZViZV7b3NWAPnx/7zuaDgPP5V/2
ESCAPE EVERY $
Docker Compose treats
$
as variable interpolation. When pasting into
docker-compose.yml
, every
$
becomes
$$
Miss one and basic auth will loop you.
akvorado-lab · don jolley
slide 50

## Slide 49
§ 07 harden
traefik
ENV VARS UNDER TRAEFIK SERVICE
Three entrypoints. One redirect. One ACME resolver.
# public :80 → redirect to https TRAEFIK_ENTRYPOINTS_public_HTTP_REDIRECTIONS_ENTRYPOINT_TO: websecure TRAEFIK_ENTRYPOINTS_public_HTTP_REDIRECTIONS_ENTRYPOINT_SCHEME: https # websecure :8443 with basic-auth + compress middleware TRAEFIK_ENTRYPOINTS_websecure_ADDRESS: ":8443" TRAEFIK_ENTRYPOINTS_websecure_HTTP_MIDDLEWARES: compress@docker,basic-auth@docker # let's encrypt TRAEFIK_CERTIFICATESRESOLVERS_letsencrypt_ACME_EMAIL: "email@example.com" TRAEFIK_CERTIFICATESRESOLVERS_letsencrypt_ACME_STORAGE: "/letsencrypt/acme.json" TRAEFIK_CERTIFICATESRESOLVERS_letsencrypt_ACME_HTTPCHALLENGE_ENTRYPOINT: "public"
Plus a basic-auth middleware label with your escaped hash, and akvorado-letsencrypt mounted at /letsencrypt.
akvorado-lab · don jolley
slide 51

## Slide 50
§ 07 harden
console · https
AKVORADO-CONSOLE · LABELS
Switch the console router to HTTPS.
labels:
- traefik.enable=
true # enable TLS, attach the cert resolver, declare the domain - traefik.http.routers.akvorado-console.tls= true - traefik.http.routers.akvorado-console.tls.certresolver=letsencrypt - traefik.http.routers.akvorado-console.tls.domains[ 0].main=flows.example.com # move the console off the public entrypoint onto websecure - traefik.http.routers.akvorado-console.entrypoints= websecure
The Remote-User / Remote-Name / Remote-Email headers are static under basic auth — set them to whoever owns the dashboard.
akvorado-lab · don jolley
slide 52

## Slide 51
§ 07 harden
apply
RECREATE · DON'T RESTART
Apply the compose change.
# open the standard ports $ sudo ufw allow 80/tcp $ sudo ufw allow 443 /tcp # recreate only traefik + console $ docker compose up -d --force-recreate \
traefik akvorado-console
# watch the cert get issued $ docker compose logs -f traefik \
| grep -i
"acme\|certificate\|tls\|error"
Hit https://flows.example.com — you should get a basic-auth prompt and a valid Let's Encrypt cert.
akvorado-lab · don jolley
slide 53

## Slide 52
§ 07 harden
troubleshoot
FIVE THINGS THAT USUALLY BREAK IT
HTTPS troubleshooting.
SYMPTOM
LIKELY CAUSE
CHECK
Cert not issued
DNS not resolving to VM
dig flows.example.com
Cert not issued
Port 80 not reachable
Firewall / ISP inbound :80
"Invalid certificate"
Traefik still starting
docker compose logs traefik
401 Unauthorized loop
$$ not escaped in hash
Re-check the basicauth label
HTTP not redirecting
Redirect env vars missing
Inspect traefik environment
akvorado-lab · don jolley
slide 54

## Slide 53
Lazy way
Delete the current ./docker/docker-compose.yaml on your VM
Copy from the lab git repo the ./docker/docker-compose-https.ymal to your local ./docker/docker-compose.yaml
Replace your existing docker-compose.yaml with the premade docker-compose-https.yaml

## Slide 54
§ 08
Tear it down.
Clean removal — for the next lab session, or when a clean reinstall is faster than debugging.

## Slide 55
§ 08 tear down
cleanup
FOUR STEPS · LAST ONE OPTIONAL
Removing Akvorado from the VM.
01
docker compose down -v
Containers, networks, and data volumes (ClickHouse) — the -v is what wipes the data.
02
rm -rf ~/akvorado
Config files and the working directory.
03
docker image prune -a
Cached images you no longer need.
04
apt purge docker-ce …
Optional. Only if you want Docker itself off the VM.
DON'T USE DOCKER SYSTEM PRUNE --VOLUMES IF
other Docker projects share this VM. It removes everything Docker-related, not just Akvorado.
akvorado-lab · don jolley
slide 56

## Slide 56
recap
what you built
TWO HOURS LATER
What you walked out with.
A RUNNING STACK
Akvorado · ClickHouse · Kafka, in Docker.
UI live on
:8081
.
FLOWS IN THE PIPE
At least one router or switch exporting
NetFlow or sFlow into your collector.
THE RIGHT N
Intuition for sample rate trade-offs
across switch, collector, and disk.
A PATH TO PRODUCTION
Traefik + Let's Encrypt + basic auth,
ready when you leave the lab.
akvorado-lab · don jolley
slide 57

## Slide 57
QUESTIONS · REFERENCES
Questions?
akvorado.net/docs · github.com/akvorado/akvorado · lab guide in your pack
https://github.com/donaldwolcomm/a-lab/
Don Jolley · ZANOG · thanks for coming
end of deck